## Slide 1: AP-Side AoA-Assisted Dynamic RTS Threshold Adaptation for Hidden-Node in Wi-Fi
Professor Chien-Chao Tseng
Department of Computer Science
National Yang Ming Chiao Tung University
cctseng@cs.nycu.edu.tw

## Slide 2: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 3: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 4: Hidden Nodes Problem and RTS/CTS
Hidden Node Problem
  Devices can communicate with AP but cannot detect each other
  When they transmit at the same time, their signals collide at the AP
    Causes packet loss and lower throughput
Request To Send / Clear To Send (RTS/CTS)
  Optional 802.11 handshake before data transmission
  Makes nearby and hidden nodes defer, reducing collisions

## Slide 5: RTS/CTS Workflow
RTS Threshold:
RTS/CTS 只有在封包大於這個 RTS Threshold的時候才會使用
Step:
  Sender sends RTS to request channel access
    Nearby node hearing RTS defers
  AP sends CTS to grant transmission permission
    Hidden node hearing CTS defers
  Sender transmits data after the channel is reserved
1. RTS
2. CTS
3. DATA
2. CTS
Sender
AP
Hidden Node
1. RTS
Nearby Node
Request To Send / Clear To Send (RTS/CTS)
Notes: RTS Threshold 是專有名詞
The use of the RTS/CTS mechanism is under control of the dot11RTSThreshold attribute. This attribute maybe set on a per-STA basis. This mechanism allows STAs to be configured to initiate RTS/CTS either always,never, or only on frames longer than a specified length.
https://mrncciew.com/wp-content/uploads/2014/10/ieee-802-11-2012.pdf#page=5.00

## Slide 6: RTS Threshold Tuning
RTS/CTS handshake can also negatively impact performance sinceit introduces additional delay and overhead
standard does not specify what RTS threshold to use
There arealso cases where the RT value is set to the maximum frame size, sothat RTS/CTS is never used. However, 802.11 product manufacturers make recommendations to users that if they are experiencingdegraded performance, they should test their network with lowerRT values.
Could a better fixed value fix it? No single one fits all:
  Too low → RTS/CTS everywhere → overhead even without hidden nodes
  Too high → hidden-node collisions unprotected

## Slide 7: Related Work
a number of studieshave explored techniques to dynamically set the value of the RT
investigates throughputperformance when using or not using RTS/CTS and have advocatedboth for and against the use of RTS/CTS
  How effective is the IEEE 802.11 RTS/CTS handshake in ad hoc networks
explored how to dynamically set the RTSThreshold, RT
  [9] Laura Huei-jiun Ju and Izhak Rubin. 2003. “The Effect of Disengaging RTS/CTS Dialogue in IEEE 802.11 MAC Protocol.” In International Conference on Wireless Networks, pp. 632–638.
  A new dynamic scheme for efficient RTS threshold handling in wireless networks
  A machine learning approach for dynamic control of RTS/CTS in WLANs

## Slide 8
Prior work already tunes RTS/CTS dynamically with modified nodes:
  On/off per frame — from contention [Edalat '18]
  Tune the threshold value — from packet size / loss [Ahsan '10, AINA ‘08]
  For/against analyses: RTS/CTS helps only sometimes [Ju&Rubin '03, Xu ’02]
Common shape:
  Each node self-tunes from its OWN link stats (loss, traffic)
  Distributed, per-node — set at the transmitter, no AP coordinationqw

## Slide 9: Location Info Unused for RTS Control
Adaptive RTS threshold control already exists
  Switch RTS/CTS on or off per frame
  Tune the RTS threshold value
Prior work relies on link information only
  E.g., Loss statistics or traffic models
No design uses location information
Notes: 要加上前面為什麼有人要調整 rts threshold
Aware sta location 是比 Move 正確的說法
----
論文都很舊 2006年

## Slide 10: What every prior design misses — two blind spots:
1. Non-spatial
  uses link info only (loss / traffic); never WHO is hidden from whom
Per-node & blind to the global picture
  a self-tuning STA can't see its own hidden peers (by definition unheard) → can't separate hidden from contention, can't coordinate across STAs

## Slide 11: AP-side, global, spatial
Prior work also modifies stations — but makes each a full self-tuner. We keep the STA thin: the AP is the single brain with the global spatial view; the STA only applies the threshold it is told.
AP Sense Environment
  Collect CSI
    Estimate STA direction
  Collect link information
AP Evaluate Risk
AP Update all STAs Threshold
Sense Environment
Evaluate
Risk
Update Threshold
Notes: 只能控制 AP side的RTS threshold是問題嗎?

## Slide 12: Outline
Introduction
Background
  Complex Baseband Signal
  Channel State Information
  AoA
  Steering Vector
  MUSIC
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 13: Story
STA send data to AP
And AP calculate AoA
Path 1
Path 2
Path 3

## Slide 14: Carrier
Represented as a complex exponential
: Amplitude — signal strength relative to known transmitted wave
: Phase — signal’s rotation relative to a known transmitted wave
Notes: https://www.sciencedirect.com/topics/engineering/phasor-representation
CSI=transmitted reference signal / received signal​

## Slide 15: Angle of Arrival (AoA): STA Direction
AoA tells STA's direction
AP measures AoA from normal uplink frames
Rays from a distant STA arrive parallel
  Both antennas see the same angle
d
θ
θ
Notes: 天線可以調嗎? 可以調的話會改變 AoA

## Slide 16: Wi-Fi Channel State Information (CSI)
Describes propagation process of the wireless signal
  Contains geometric information
CSI is estimated from a known pattern
  Sender transmits a pattern known to receiver
  Receiver estimates CSI from received pattern
Path 1
Path 2
Path 3

## Slide 17: Steering Vector: Direction's Fingerprint
Antennas hear signal at slightly different times
Each AoA has a predictable arrival pattern
  Predicted pattern is Steering Vector
Compare measured CSI with every fingerprint
  The best match is the AoA
d
θ
d
2
Notes: AP 天線可調整方向 會影響 Steering Vector 的計算或正確性嗎?

## Slide 18: Multiple Signal Classification (MUSIC)
MUSIC is algorithm that estimates AoA from CSI
  Widely used in Wi-Fi localization
MUSIC matches every angle's steering vector to CSI
  Matching produces a spatial spectrum
  Peaks indicate likely AoAs

## Slide 19: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 20: Hidden-Node Risk Score
Risk computed for each active STA pair
  Geometric information
    AoA between two active STAs
  Link information
    Retry rate / RSSI / MCS / traffic activity
Risks aggregate into a BSS-level score
If the risk score over/less than a number change the rts threshold

## Slide 21: Risk-Driven RTS Threshold Adaptation
The RTS Threshold value use - 標題:"(Exploiting) Packet Distribution based Tuning of RTS Threshold in IEEE 802.11"- 發表:ISCC '10(IEEE Symposium on Computers and Communications, 2010) method

## Slide 22: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 23: Evaluation
Scenarios
  Hidden-node
  Non-hidden-node
Threshold Control Policy
  Static RTS threshold
  Dynamic RTS threshold
  Disable RTS/CTS
Metrics
  Throughput
  Retry rate
  Latency

## Slide 24: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 25: Next Steps
Define risk scoring and score-to-threshold mapping
  Reinforcement learning?
Adopt other MUSIC variant for AoA estimation
Speed up MUSIC
Define evaluation scenarios, baselines, and metrics

## Slide 26: Appendix

## Slide 27: RTS/CTS Mitigates Hidden-Node Collisions
1. RTS
2. CTS
4. DATA
5. ACK
2. CTS

## Slide 28: RTS/CTS Mitigates Hidden-Node Collisions
Optional 802.11 handshake before data transmission
RTS/CTS makes nearby nodes defer, reducing hidden-node collisions
Step:
  Sender sends RTS to request channel access
    Nearby node hearing RTS defers
  AP sends CTS to grant transmission permission
    Hidden node hearing CTS defers
  Sender transmits data after the channel is reserved
1. RTS
2. CTS
3. DATA
2. CTS
Sender
AP
Hidden Node
1. RTS
Nearby Node
Request To Send / Clear To Send (RTS/CTS)

## Slide 29: Antenna Timing Differences Reveal AoA
Antennas hear signal at slightly different times
Wave arrival pattern depends only on direction
Reading the pattern from CSI gives the AoA
d
θ
θ

## Slide 30: CSI Representation
Represented as a complex exponential
: Amplitude — signal strength relative to known transmitted wave
: Phase — signal’s rotation relative to a known transmitted wave
Notes: https://www.sciencedirect.com/topics/engineering/phasor-representation
CSI=transmitted reference signal / received signal​

## Slide 31: Spatial Spectrum Estimation Estimates AoA
Spatial spectrum estimation scores each angle by matching phase pattern to CSI
  Phase pattern of each angle is called steering vector
Angle with the highest score is most likely signal's AoA
  Multipath yields multiple peaks
Notes: https://www.sciencedirect.com/science/article/pii/S209099771300031X

## Slide 32: Classic Beamforming Hits a Resolution Wall
The straightforward scorer: shift each antenna's signal to align with a candidate angle, then sum - a true arrival from that angle adds up in phase (delay-and-sum beamforming)
Sweeping this listening beam across all angles gives the spatial spectrum - like turning an ear toward each direction
The beam's width is set by array size: with only 2-4 antennas it is roughly 60 degrees wide
Indoor paths arrive just 10-20 degrees apart, so they merge into one blob inside the wide beam
More antennas would sharpen the beam - but a commodity AP's antenna count is fixed

## Slide 33: Why We Use MUSIC
MUSIC skips the beam entirely: it exploits the statistical structure of the received signal to test each angle directly, so resolution is not capped by antenna count
Faster alternatives fit poorly: ESPRIT's algebraic shortcut exists only for strictly regular arrays and degrades under heavy multipath; exhaustive-search ML is accurate but computationally infeasible
MUSIC works with any known antenna layout and stays robust in multipath; its heavier computation is affordable since localization does not need fast updates
Proven on our hardware class: SpotFi reaches ~40 cm median accuracy with 3 antennas using MUSIC
We therefore adopt MUSIC for AP-side AoA estimation

## Slide 34: LRG1 Provides AP-Side Control and Measurements
LRG1 exposes the RTS threshold as the main AP-side control knob.
AP-side measurements include retry statistics, RSSI, CSI, AoA, and MCS.

## Slide 35: Performance Analysis Separates Gains from Limits
Analyze when the method improves performance and when its benefit is limited.