## Slide 1: AoA-Assisted Dynamic RTS Threshold Adaptation for Hidden-Node Risk Mitigation in Wi-Fi
Professor Chien-Chao Tseng
Department of Computer Science
National Yang Ming Chiao Tung University
cctseng@cs.nycu.edu.tw

## Slide 2: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 3: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 4: Hidden Nodes Problem
Devices can communicate with AP but cannot detect each other
When they transmit at the same time, their signals collide at the AP
  Causes packet loss and lower throughput

## Slide 5: RTS/CTS Mitigates Hidden-Node Collisions
Optional 802.11 handshake before data transmission
RTS/CTS makes nearby nodes defer, reducing hidden-node collisions
Step:
  Sender sends RTS to request channel access
    Nearby node hearing RTS defers
  AP sends CTS to grant transmission permission
    Hidden node hearing CTS defers
  Sender transmits data after the channel is reserved
1. RTS
2. CTS
3. DATA
2. CTS
Sender
AP
Hidden Node
1. RTS
Nearby Node
Request To Send / Clear To Send (RTS/CTS)

## Slide 6: Limitations of Static RTS Thresholds
Conventional 802.11 usually uses a fixed RTS threshold
A static threshold cannot adapt to changing node locations

## Slide 7: Spatially Aware Dynamic RTS Threshold Using AoA
AoA provides spatial cues about relative directions of stations
AP combines AoA with link information to estimate hidden-node risk
Estimated risk guides dynamic RTS threshold adjustment
Angle of Arrival (AoA)
Notes: 只能控制 AP side的RTS threshold是問題嗎?

## Slide 8: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 9: Wi-Fi Channel State Information (CSI)
Describes propagation process of the wireless signal
  Therefore, contains geometric information of the propagation space
Sender transmits a pattern known to receiver
The receiver estimates CSI for each subcarrier and transmit-receive antenna pair
Path 1
Path 2
Path 3

## Slide 10: Angle of Arrival (AoA)
AoA is the wave receive angle by antenna
AoA is the space information get from CSI
  The get method is from Steering Vector
d
θ
θ

## Slide 11: Steering Vector
Plane waves reach each antenna at different distances from angle
Steering Vector is a vector storing the
This differences is fixed in idea env
d
θ
d
2

## Slide 12: Multiple Signal Classification (MUSIC)
MUSIC is a spatial spectrum estimator built on CSI and steering vectors
  Invented in 1979
  Widely used in Wi-Fi localization

## Slide 13: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 14: AoA-Assisted Dynamic RTS Threshold Adaptation
Estimate each STA's AoA from AP-side CSI
Combines AoA with RSSI, MCS, and traffic activity to assess hidden-node risk
Adjust RTS threshold based on the risk score
  High risk → lower RTS threshold
  Low risk → raise RTS threshold
Distribute updated threshold to all STAs

## Slide 15: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 16: Evaluation
Scenarios
  Hidden-node
  Non-hidden-node
Threshold Control Policy
  Static RTS threshold
  Dynamic RTS threshold
  Disable RTS/CTS
Metrics
  Throughput
  Retry rate
  Latency
  MCS

## Slide 17: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 18: Next Steps
Adopt SpotFi's MUSIC variant for AoA estimation
  SpotFi (ACM SIGCOMM CCR 45(4), Aug 2015)
Speed up eigen decomposition
Define risk scoring and score-to-threshold mapping
  Reinforcement learning?
Define evaluation scenarios, baselines, and metrics

## Slide 19: Appendix

## Slide 20: RTS/CTS Mitigates Hidden-Node Collisions
1. RTS
2. CTS
4. DATA
5. ACK
2. CTS

## Slide 21: CSI Representation
Represented as a complex exponential
: Amplitude — signal strength relative to known transmitted wave
: Phase — signal’s rotation relative to a known transmitted wave
Notes: https://www.sciencedirect.com/topics/engineering/phasor-representation
CSI=transmitted reference signal / received signal​

## Slide 22: Spatial Spectrum Estimation Estimates AoA
Spatial spectrum estimation scores each angle by matching phase pattern to CSI
  Phase pattern of each angle is called steering vector
Angle with the highest score is most likely signal's AoA
  Multipath yields multiple peaks
Notes: https://www.sciencedirect.com/science/article/pii/S209099771300031X

## Slide 23: Classic Beamforming Hits a Resolution Wall
The straightforward scorer: shift each antenna's signal to align with a candidate angle, then sum - a true arrival from that angle adds up in phase (delay-and-sum beamforming)
Sweeping this listening beam across all angles gives the spatial spectrum - like turning an ear toward each direction
The beam's width is set by array size: with only 2-4 antennas it is roughly 60 degrees wide
Indoor paths arrive just 10-20 degrees apart, so they merge into one blob inside the wide beam
More antennas would sharpen the beam - but a commodity AP's antenna count is fixed

## Slide 24: Why We Use MUSIC
MUSIC skips the beam entirely: it exploits the statistical structure of the received signal to test each angle directly, so resolution is not capped by antenna count
Faster alternatives fit poorly: ESPRIT's algebraic shortcut exists only for strictly regular arrays and degrades under heavy multipath; exhaustive-search ML is accurate but computationally infeasible
MUSIC works with any known antenna layout and stays robust in multipath; its heavier computation is affordable since localization does not need fast updates
Proven on our hardware class: SpotFi reaches ~40 cm median accuracy with 3 antennas using MUSIC
We therefore adopt MUSIC for AP-side AoA estimation

## Slide 25: LRG1 Provides AP-Side Control and Measurements
LRG1 exposes the RTS threshold as the main AP-side control knob.
AP-side measurements include retry statistics, RSSI, CSI, AoA, and MCS.

## Slide 26: Performance Analysis Separates Gains from Limits
Analyze when the method improves performance and when its benefit is limited.