## Slide 1: AoA-Assisted Dynamic RTS Threshold Adaptation for Hidden-Node Risk Mitigation in Wi-Fi
Professor Chien-Chao Tseng
Department of Computer Science
National Yang Ming Chiao Tung University
cctseng@cs.nycu.edu.tw

## Slide 2: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 3: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 4: Hidden Nodes Problem
Devices can communicate with AP but cannot detect each other
When they transmit at the same time, their signals collide at the AP
  Causes packet loss and lower throughput

## Slide 5: RTS/CTS Mitigates Hidden-Node Collisions
Optional 802.11 handshake before data transmission
RTS/CTS makes nearby nodes defer, reducing hidden-node collisions
Step:
  Sender sends RTS to request channel access
    Nearby node hearing RTS defers
  AP sends CTS to grant transmission permission
    Hidden node hearing CTS defers
  Sender transmits data after the channel is reserved
1. RTS
2. CTS
3. DATA
2. CTS
Sender
AP
Hidden Node
1. RTS
Nearby Node
Request To Send / Clear To Send (RTS/CTS)

## Slide 6: No Static RTS Threshold Fits All Scenarios
RTS/CTS is used only for frames above threshold
Commodity APs use one fixed threshold
Suitable threshold changes as nodes move
A fixed value falls below or above the suitable value
  Below → RTS/CTS overhead even without hidden nodes
  Above → Hidden-node collisions stay unresolved

## Slide 7: Location Info Unused for RTS Control
Adaptive RTS threshold control already exists
  Switch RTS/CTS on or off per frame
  Tune the RTS threshold value
Prior work relies on link information only
  E.g., Loss statistics or traffic models
No design uses location information

## Slide 8: Spatially Aware Dynamic RTS Threshold
Angle of Arrival (AoA) is direction a signal arrives from
  Reveals node’s relative directions
AP combines STA’s AoA with link information to estimate hidden-node risk
Estimated risk guides dynamic RTS threshold adjustment
Pay RTS/CTS overhead only when risk justifies it
Notes: 只能控制 AP side的RTS threshold是問題嗎?

## Slide 9: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 10: Wi-Fi Channel State Information (CSI)
Describes propagation process of the wireless signal
  Contains geometric information
Sender transmits a pattern known to receiver
Receiver estimates CSI from received pattern
Path 1
Path 2
Path 3

## Slide 11: Steering Vector: Direction's Fingerprint
Antennas hear signal at slightly different times
Each AoA has a predictable arrival pattern
  Predicted pattern is Steering Vector
Compare measured CSI with every fingerprint
  The best match is the AoA
d
θ
d
2

## Slide 12: Multiple Signal Classification (MUSIC)
MUSIC is algorithm that estimates AoA from CSI
  Widely used in Wi-Fi localization
MUSIC matches every angle's steering vector to CSI
  Matching produces a spatial spectrum
  Peaks indicate likely AoAs

## Slide 13: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 14: AoA-Assisted Dynamic RTS Threshold Adaptation
Collect CSI
Estimate AoA with MUSIC
Score pair-level hidden-node risk
Aggregate risk to BSS level
Update RTS threshold
Sync threshold to all STAs

## Slide 15: Hidden-Node Risk Score
Pair-level risk computed for each active STA pair
  Geometric information
    AoA between two active STAs
  Link information
    Retry rate / RSSI / MCS / traffic activity
Pair risks aggregate into a BSS-level score

## Slide 16: Risk-Driven RTS Threshold Adaptation
High risk → lower the RTS threshold
  Protect more frames
Low risk → raise/restore the threshold
  Avoid unnecessary overhead

## Slide 17: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 18: Evaluation
Scenarios
  Hidden-node
  Non-hidden-node
Threshold Control Policy
  Static RTS threshold
  Dynamic RTS threshold
  Disable RTS/CTS
Metrics
  Throughput
  Retry rate
  Latency

## Slide 19: Outline
Introduction
Background
AoA-Assisted Dynamic RTS Threshold Adaptation
Evaluation
Conclusion

## Slide 20: Next Steps
Adopt other MUSIC variant for AoA estimation
Speed up MUSIC
Define risk scoring and score-to-threshold mapping
  Reinforcement learning?
Define evaluation scenarios, baselines, and metrics

## Slide 21: Appendix

## Slide 22: RTS/CTS Mitigates Hidden-Node Collisions
1. RTS
2. CTS
4. DATA
5. ACK
2. CTS

## Slide 23: Antenna Timing Differences Reveal AoA
Antennas hear signal at slightly different times
Wave arrival pattern depends only on direction
Reading the pattern from CSI gives the AoA
d
θ
θ

## Slide 24: CSI Representation
Represented as a complex exponential
: Amplitude — signal strength relative to known transmitted wave
: Phase — signal’s rotation relative to a known transmitted wave
Notes: https://www.sciencedirect.com/topics/engineering/phasor-representation
CSI=transmitted reference signal / received signal​

## Slide 25: Spatial Spectrum Estimation Estimates AoA
Spatial spectrum estimation scores each angle by matching phase pattern to CSI
  Phase pattern of each angle is called steering vector
Angle with the highest score is most likely signal's AoA
  Multipath yields multiple peaks
Notes: https://www.sciencedirect.com/science/article/pii/S209099771300031X

## Slide 26: Classic Beamforming Hits a Resolution Wall
The straightforward scorer: shift each antenna's signal to align with a candidate angle, then sum - a true arrival from that angle adds up in phase (delay-and-sum beamforming)
Sweeping this listening beam across all angles gives the spatial spectrum - like turning an ear toward each direction
The beam's width is set by array size: with only 2-4 antennas it is roughly 60 degrees wide
Indoor paths arrive just 10-20 degrees apart, so they merge into one blob inside the wide beam
More antennas would sharpen the beam - but a commodity AP's antenna count is fixed

## Slide 27: Why We Use MUSIC
MUSIC skips the beam entirely: it exploits the statistical structure of the received signal to test each angle directly, so resolution is not capped by antenna count
Faster alternatives fit poorly: ESPRIT's algebraic shortcut exists only for strictly regular arrays and degrades under heavy multipath; exhaustive-search ML is accurate but computationally infeasible
MUSIC works with any known antenna layout and stays robust in multipath; its heavier computation is affordable since localization does not need fast updates
Proven on our hardware class: SpotFi reaches ~40 cm median accuracy with 3 antennas using MUSIC
We therefore adopt MUSIC for AP-side AoA estimation

## Slide 28: LRG1 Provides AP-Side Control and Measurements
LRG1 exposes the RTS threshold as the main AP-side control knob.
AP-side measurements include retry statistics, RSSI, CSI, AoA, and MCS.

## Slide 29: Performance Analysis Separates Gains from Limits
Analyze when the method improves performance and when its benefit is limited.